## Slide 1
SIEMENS ENERGY
CONFIDENTIAL
SUBCONTRACTOR EHS NON-COMPLIANCE & SAFETY VIOLATION REPORT
BOXED FORMAT WITH PHOTO PLACEHOLDERS - ENGLISH VERSION
Project: KAZ Power Plant Upgrade Project Reference: SE-EHS-NC-2026-001 BOXED V3 ENGLISH Date: September 2026 Prepared by: EHS Manager - Siemens Energy Classification: Confidential - Management Eyes Only FORMAT OVERVIEW: • 12 Slides Total • Each Observation Slide = 5 Distinct Boxes • Box 1: Non-Compliance Details (with location/date fields) • Box 2 & 3: Photo Evidence Placeholders - 2 photos per violation • Box 4: Risk Level & Impact (Red=Critical, Amber=High) • Box 5: Required Corrective Action + Standard Reference STANDARDS: ISO 45001:2018, ISO 14001:2015, OSHA, SE EHS Requirements
HOW TO USE THIS TEMPLATE - INSTRUCTIONS
1. For each violation slide, fill Box 1 with specific details: - Location, Date, Time, Equipment ID - Replace [Insert...] placeholders 2. Box 2 & 3 - Photo Placeholders: - Drag & drop your site photos directly into the boxes - Photo 1: Overview / wide shot - Photo 2: Close-up / different angle - Add Fig number, date, GPS coordinates 3. Box 4 - Risk is pre-filled - color-coded: - RED = CRITICAL (fatality potential) - AMBER = HIGH (serious injury / env) 4. Box 5 - Corrective actions are actionable: - Assign owner and deadline - Track closure in NCR system 5. Final Slide: Action Plan with 4 Boxes: - Immediate (0-24h), Short (1-7d), Strategic (7-30d) - Management Decision Matrix with Yes/No checkboxes VISUAL DESIGN: • Background: Deep Petrol #0E2F3E • Boxes: Card #143D4E + White for actions • Photo boxes: Dark #0A222B with dashed border effect • All boxes have titles for clarity
Zero Harm is Non-Negotiable | 5 Boxes Per Slide | 2 Photo Placeholders Per Violation | English Version | Ready for Management Review

## Slide 2
01
01 - UNAUTHORIZED WORK - WITHOUT PERMIT TO WORK (PTW)
RISK: CRITICAL
BOX 1: NON-COMPLIANCE DETAILS - Insert Location/Date/Time
Location: [Insert Area] | Date: [Insert Date] | Time: [Insert Time]
Activity: Excavation / Mechanical / Hot Work executed without approved PTW
Violation: No TRA review, no energy isolation verification, no SIMOPS coordination
PTW logbook not maintained, permit not displayed at work front as required
Reference: Siemens Energy EHS General Requirements Sec 5.3, KAZ EHS Plan Sec 7.2, ISO 45001 Cl 8.1.2
BOX 2: PHOTO EVIDENCE 1
PHOTO 1: Work activity without PTW displayed at work front [ INSERT PHOTO HERE ] DRAG & DROP YOUR SITE PHOTO Fig 01.1 Add: Date, Time, Location, GPS
BOX 3: PHOTO EVIDENCE 2
PHOTO 2: PTW logbook - missing entry / permit not available [ INSERT PHOTO HERE ] DRAG & DROP YOUR SITE PHOTO Fig 01.2 Add: Close-up / Different Angle
BOX 4: RISK LEVEL & IMPACT - CRITICAL
Potential fatality, uncontrolled hazardous energy release, fire/explosion, SIMOPS conflict. Total loss of primary control barrier. Authority may issue prohibition notice.
BOX 5: REQUIRED CORRECTIVE ACTION
1. IMMEDIATE STOP WORK - secure area and remove workforce
2. Mandatory PTW re-training for all supervisors within 24h - competency test
3. Issue formal NCR Level 1 + contractual warning letter
4. Daily PTW audit and spot-checks for 14 days - EHS verification
5. Enforce 3-strikes removal policy for non-compliant supervisors
STANDARD REF
• ISO 45001:2018 • ISO 14001:2015 • OSHA 29 CFR 1926 • SE EHS Contractor Req • Project EHS Plan • Local EPA / HSG 176 • SE-GEN-EHS-007
Siemens Energy | Zero Harm | Confidential | Boxed Format - 5 Boxes + 2 Photo Placeholders Per Slide
Slide 01 | SE-EHS-NC-2026

## Slide 3
02
02 - SITE ACCESS & INDUCTION - PERSONNEL WITHOUT EHS INDUCTION
RISK: CRITICAL
BOX 1: NON-COMPLIANCE DETAILS - Insert Location/Date/Time
No. of persons: [8-12] found working without induction card / sticker
Gate register vs actual headcount mismatch - onboarding register incomplete
No induction verification at main gate - Security-EHS interface failure
Violation: KAZ Project EHS Plan Sec 6.1 Competency & Training, local labor law
Systemic failure in access control and subcontractor self-verification
BOX 2: PHOTO EVIDENCE 1
PHOTO 1: Workers without induction cards - site overview [ INSERT PHOTO HERE ] DRAG & DROP YOUR SITE PHOTO Fig 02.1 Add: Date, Time, Location, GPS
BOX 3: PHOTO EVIDENCE 2
PHOTO 2: Gate register vs induction cards verification [ INSERT PHOTO HERE ] DRAG & DROP YOUR SITE PHOTO Fig 02.2 Add: Close-up / Different Angle
BOX 4: RISK LEVEL & IMPACT - CRITICAL
Workers unaware of site hazards, emergency assembly points, muster procedures, life-saving rules. High probability of unsafe acts, delayed emergency response, regulatory stoppage.
BOX 5: REQUIRED CORRECTIVE ACTION
1. Immediate removal of all non-inducted personnel from site - escort by Security
2. Implement 100% gate check - Joint Security + EHS verification - No card, no entry
3. Subcontractor to submit full manpower list vs induction records within 12h + gap closure plan
4. Introduce QR / Biometric induction tracking linked to access control
5. Formal warning + back-charge for re-induction sessions
STANDARD REF
• ISO 45001:2018 • ISO 14001:2015 • OSHA 29 CFR 1926 • SE EHS Contractor Req • Project EHS Plan • Local EPA / HSG 176 • SE-GEN-EHS-007
Siemens Energy | Zero Harm | Confidential | Boxed Format - 5 Boxes + 2 Photo Placeholders Per Slide
Slide 02 | SE-EHS-NC-2026

## Slide 4
03
03 - PPE NON-COMPLIANCE - FAILURE TO WEAR MANDATORY PPE
RISK: HIGH
BOX 1: NON-COMPLIANCE DETAILS - Insert Location/Date/Time
PPE missing: Helmet chin strap not secured, safety glasses, gloves, hi-vis vest not worn
Location: [Insert Location] | Task: [Insert Task] | Date: [Insert Date]
Subcontractor supervision present on site but failing to enforce compliance
PPE available in store - confirms behavioral and supervisory failure, not availability
Violation: Siemens Energy Life Saving Rule #3, PPE Standard EN 397, EN 166, ANSI Z89.1
BOX 2: PHOTO EVIDENCE 1
PHOTO 1: PPE violation - wide shot showing multiple workers [ INSERT PHOTO HERE ] DRAG & DROP YOUR SITE PHOTO Fig 03.1 Add: Date, Time, Location, GPS
BOX 3: PHOTO EVIDENCE 2
PHOTO 2: PPE violation - close-up + supervisor present not enforcing [ INSERT PHOTO HERE ] DRAG & DROP YOUR SITE PHOTO Fig 03.2 Add: Close-up / Different Angle
BOX 4: RISK LEVEL & IMPACT - HIGH
Immediate risk of head injury, eye injury, hand lacerations, struck-by incidents. Demonstrates weak safety culture. Significantly increases LTIFR/TRIR.
BOX 5: REQUIRED CORRECTIVE ACTION
1. On-the-spot correction + toolbox talk - documented with photos and attendance
2. Issue Safety Observation Cards + formal EHS violation notice to individual and supervisor
3. Mandatory PPE compliance campaign - daily checks at start of shift + random checks
4. Link PPE compliance to subcontractor KPI and payment milestone - weekly scorecard
5. Supervisor accountability briefing - 3-strikes removal policy signed
STANDARD REF
• ISO 45001:2018 • ISO 14001:2015 • OSHA 29 CFR 1926 • SE EHS Contractor Req • Project EHS Plan • Local EPA / HSG 176 • SE-GEN-EHS-007
Siemens Energy | Zero Harm | Confidential | Boxed Format - 5 Boxes + 2 Photo Placeholders Per Slide
Slide 03 | SE-EHS-NC-2026

## Slide 5
04
04 - EXCAVATION SAFETY - INADEQUATE HARD BARRICADES & PROTECTION
RISK: CRITICAL
BOX 1: NON-COMPLIANCE DETAILS - Insert Location/Date/Time
Depth: [1.2m - 2.5m observed] - No hard barricade, only loose warning tape (prohibited for >1.2m)
No edge protection, no safe access/egress (ladders missing), spoil pile within 1m of edge
No reflective markers, delineators, or lighting for night-time visibility
Violation: OSHA 29 CFR 1926 Subpart P, ISO 45001 Excavation Standard, Siemens SE-GEN-EHS-007
Night work risk: Excavation invisible - vehicle fall hazard
BOX 2: PHOTO EVIDENCE 1
PHOTO 1: Excavation without hard barricade - full view with tape only [ INSERT PHOTO HERE ] DRAG & DROP YOUR SITE PHOTO Fig 04.1 Add: Date, Time, Location, GPS
BOX 3: PHOTO EVIDENCE 2
PHOTO 2: Spoil pile too close to edge + no ladder - close view [ INSERT PHOTO HERE ] DRAG & DROP YOUR SITE PHOTO Fig 04.2 Add: Close-up / Different Angle
BOX 4: RISK LEVEL & IMPACT - CRITICAL
High potential for fatal fall into excavation, cave-in engulfment, personnel/vehicle fall. Excavation is High-Risk activity with fatality history - classified as Major Accident Hazard.
BOX 5: REQUIRED CORRECTIVE ACTION
1. IMMEDIATE hard barricading - scaffold tubes / concrete barriers / hard fencing around all excavations
2. Provide compliant access ladders every 7.5m + keep spoil minimum 1.5m away + toe boards
3. Excavation permit re-validation with geotechnical check and competent person inspection
4. Install reflective delineators + solar blinker lights for low-light hours
5. Competent person inspection checklist daily before start - signed by engineer + verified by SE EHS
STANDARD REF
• ISO 45001:2018 • ISO 14001:2015 • OSHA 29 CFR 1926 • SE EHS Contractor Req • Project EHS Plan • Local EPA / HSG 176 • SE-GEN-EHS-007
Siemens Energy | Zero Harm | Confidential | Boxed Format - 5 Boxes + 2 Photo Placeholders Per Slide
Slide 04 | SE-EHS-NC-2026

## Slide 6
05
05 - DIRECTIVES NON-COMPLIANCE - FAILURE TO FOLLOW EHS INSTRUCTIONS
RISK: HIGH
BOX 1: NON-COMPLIANCE DETAILS - Insert Location/Date/Time
Date of instruction: [Insert Date] | Instruction: [Insert EHS instruction details]
Repeated failure to comply with verbal and written EHS instructions - documented in daily reports + email trail
Toolbox Talks (TBT) not conducted or without documentation / attendance sheets / task relevance
Previous NCRs closed without evidence or verification - falsification of closure
Violation: ISO 45001 Cl 7.3 Awareness & 8.1 Operational Control - Willful disregard
BOX 2: PHOTO EVIDENCE 1
PHOTO 1: Evidence of ignored instruction (e.g., open excavation still not barricaded) [ INSERT PHOTO HERE ] DRAG & DROP YOUR SITE PHOTO Fig 05.1 Add: Date, Time, Location, GPS
BOX 3: PHOTO EVIDENCE 2
PHOTO 2: TBT register missing / NCR closure without evidence [ INSERT PHOTO HERE ] DRAG & DROP YOUR SITE PHOTO Fig 05.2 Add: Close-up / Different Angle
BOX 4: RISK LEVEL & IMPACT - HIGH
Erosion of EHS authority and safety culture. Creates precedent for further violations, normalizes deviance. If directives optional, all critical controls (LOTO, WAH) at risk of failure. Systemic cultural failure.
BOX 5: REQUIRED CORRECTIVE ACTION
1. Escalate to Project Management - formal letter to Subcontractor Top Management - require written commitment
2. Implement Daily EHS Directives Log - all instructions logged with date/time, owner, sign-off by PM + SE EHS
3. Hold EHS Leadership stand-down meeting with all foremen - documented commitment signed
4. Link non-compliance to contractual penalty clause - financial consequence
5. Weekly EHS compliance scorecard Red/Amber/Green reviewed in project management meeting
STANDARD REF
• ISO 45001:2018 • ISO 14001:2015 • OSHA 29 CFR 1926 • SE EHS Contractor Req • Project EHS Plan • Local EPA / HSG 176 • SE-GEN-EHS-007
Siemens Energy | Zero Harm | Confidential | Boxed Format - 5 Boxes + 2 Photo Placeholders Per Slide
Slide 05 | SE-EHS-NC-2026

## Slide 7
06
06 - TRAFFIC & SIGNAGE - POOR / DAMAGED / MISSING SAFETY SIGNAGE
RISK: HIGH
BOX 1: NON-COMPLIANCE DETAILS - Insert Location/Date/Time
Missing / damaged: Speed limit signs (15 km/h), parking signage, pedestrian walkway markings
Vehicle-pedestrian interface unmanaged - no flagmen at high-risk intersections and blind spots
Speeding observed: 30 km/h in construction zone (limit 15 km/h) - confirmed by radar gun
Pedestrian routes not marked or segregated - workers walking on vehicle routes
Violation: Project Traffic Management Plan (TMP), ISO 39001 Road Traffic Safety
BOX 2: PHOTO EVIDENCE 1
PHOTO 1: Missing / damaged speed limit sign - location view [ INSERT PHOTO HERE ] DRAG & DROP YOUR SITE PHOTO Fig 06.1 Add: Date, Time, Location, GPS
BOX 3: PHOTO EVIDENCE 2
PHOTO 2: No pedestrian segregation + vehicle-pedestrian interface risk [ INSERT PHOTO HERE ] DRAG & DROP YOUR SITE PHOTO Fig 06.2 Add: Close-up / Different Angle
BOX 4: RISK LEVEL & IMPACT - HIGH
High risk of vehicle-pedestrian collision, equipment damage, fatality - vehicle incidents are top 3 fatality causes. Poor signage increases liability. Emergency vehicle access may be impeded.
BOX 5: REQUIRED CORRECTIVE ACTION
1. Immediate reinstatement of all traffic signs per approved TMP - retro-reflective grade, proper height
2. Establish dedicated pedestrian routes with hard segregation - Jersey barriers + green walkway paint
3. Deploy trained flagmen at intersections + implement speed monitoring - radar checks 2x daily
4. Conduct traffic safety campaign and driver re-induction - all drivers including subcontractor
5. EHS + Logistics joint daily inspection of traffic controls - checklist signed
STANDARD REF
• ISO 45001:2018 • ISO 14001:2015 • OSHA 29 CFR 1926 • SE EHS Contractor Req • Project EHS Plan • Local EPA / HSG 176 • SE-GEN-EHS-007
Siemens Energy | Zero Harm | Confidential | Boxed Format - 5 Boxes + 2 Photo Placeholders Per Slide
Slide 06 | SE-EHS-NC-2026

## Slide 8
07
07 - WASTE MANAGEMENT - LACK OF SEGREGATION & LABELING
RISK: HIGH
BOX 1: NON-COMPLIANCE DETAILS - Insert Location/Date/Time
Waste containers without segregation - hazardous, recyclable, general waste mixed in same skip
No clear labeling, color-coding, or MSDS reference for hazardous waste bins
Oil-contaminated rags and filters disposed in general waste - environmental violation + fire hazard
Location: [Insert waste area location] | Date observed: [Insert Date]
Violation: ISO 14001:2015 Cl 8.1, Project Waste Management Plan, local EPA regulations
BOX 2: PHOTO EVIDENCE 1
PHOTO 1: Mixed waste in one container - overview showing hazardous + general [ INSERT PHOTO HERE ] DRAG & DROP YOUR SITE PHOTO Fig 07.1 Add: Date, Time, Location, GPS
BOX 3: PHOTO EVIDENCE 2
PHOTO 2: Oil-contaminated rags in general waste - close-up + fire hazard [ INSERT PHOTO HERE ] DRAG & DROP YOUR SITE PHOTO Fig 07.2 Add: Close-up / Different Angle
BOX 4: RISK LEVEL & IMPACT - HIGH
Environmental pollution risk (soil/groundwater contamination), fire hazard from incompatible mixing, regulatory fine, reputational damage to Siemens Energy. Cross-contamination makes recycling impossible - sustainability KPI failure.
BOX 5: REQUIRED CORRECTIVE ACTION
1. Immediate provision of color-coded, labeled waste skips per SE Standard: Black-General, Green-Recyclable, Red-Hazardous
2. Clean-up and correct segregation of existing mixed waste by competent team under EHS supervision
3. Training on Waste Management - hazardous waste handling, spill prevention, manifest system
4. Appoint Waste Management Focal Point from subcontractor - responsible for daily housekeeping
5. Weekly waste audit - track volumes and disposal manifests - report in monthly environmental report
STANDARD REF
• ISO 45001:2018 • ISO 14001:2015 • OSHA 29 CFR 1926 • SE EHS Contractor Req • Project EHS Plan • Local EPA / HSG 176 • SE-GEN-EHS-007
Siemens Energy | Zero Harm | Confidential | Boxed Format - 5 Boxes + 2 Photo Placeholders Per Slide
Slide 07 | SE-EHS-NC-2026

## Slide 9
08
08 - EQUIPMENT INTEGRITY - ACTIVE OIL & FUEL LEAKS FROM MACHINERY
RISK: CRITICAL
BOX 1: NON-COMPLIANCE DETAILS - Insert Location/Date/Time
Equipment: Excavator CAT 320 [ID: ___] / Loader [ID: ___] - active hydraulic oil and fuel leaks observed dripping
Drip trays not provided - soil contamination ~5 sqm observed under equipment parking area
No preventive maintenance records on site - daily inspection checklists falsified - same signature for 7 days
Violation: Equipment Safety Standard, PUWER, Environmental Protection, SE Equipment Standard
Operator competency: No evidence of daily checks by competent operator
BOX 2: PHOTO EVIDENCE 1
PHOTO 1: Active oil/fuel leak under equipment - dripping with circle highlight [ INSERT PHOTO HERE ] DRAG & DROP YOUR SITE PHOTO Fig 08.1 Add: Date, Time, Location, GPS
BOX 3: PHOTO EVIDENCE 2
PHOTO 2: Soil contamination under parking area + missing drip tray [ INSERT PHOTO HERE ] DRAG & DROP YOUR SITE PHOTO Fig 08.2 Add: Close-up / Different Angle
BOX 4: RISK LEVEL & IMPACT - CRITICAL
Fire and explosion hazard (fuel on hot surfaces), slip hazard, soil/groundwater contamination, equipment failure leading to loss of control. Breakdown of maintenance management system. Breach of ISO 14001 and PUWER.
BOX 5: REQUIRED CORRECTIVE ACTION
1. IMMEDIATE grounding of leaking equipment - Tag 'DO NOT USE - EHS HOLD' + keys removed
2. Contaminated soil to be excavated and disposed as hazardous waste - spill response with absorbents
3. Subcontractor to submit full maintenance history + third-party inspection certificates within 48h - No cert, no operation
4. Implement mandatory daily equipment checklist - verified by SE EHS/Mechanical + photo evidence of no leaks
5. Introduction of drip trays and spill kits at all equipment parking zones - 100% coverage
STANDARD REF
• ISO 45001:2018 • ISO 14001:2015 • OSHA 29 CFR 1926 • SE EHS Contractor Req • Project EHS Plan • Local EPA / HSG 176 • SE-GEN-EHS-007
Siemens Energy | Zero Harm | Confidential | Boxed Format - 5 Boxes + 2 Photo Placeholders Per Slide
Slide 08 | SE-EHS-NC-2026

## Slide 10
09
09 - HAZARDOUS MATERIAL STORAGE - DIESEL STORAGE WITHOUT SECONDARY CONTAINMENT
RISK: CRITICAL
BOX 1: NON-COMPLIANCE DETAILS - Insert Location/Date/Time
Diesel storage: Approx. 2000L (2x IBC tanks) - no secondary containment / bunding - 110% capacity required
No isolation distance from ignition sources (welding 10m away) - no fire extinguisher, no HAZCHEM signage, no spill kit
Storage on bare ground - no impervious base, no earthing/bonding for fuel transfer - static electricity risk
Direct violation: HSG 176 Storage of Flammable Liquids, EPA SPCC, SE Hazardous Materials Standard SE-ENV-003
Location: [Insert location] - Near drains / buildings - environmental receptor risk
BOX 2: PHOTO EVIDENCE 1
PHOTO 1: Diesel tanks without bunding - overview showing 2x IBC [ INSERT PHOTO HERE ] DRAG & DROP YOUR SITE PHOTO Fig 09.1 Add: Date, Time, Location, GPS
BOX 3: PHOTO EVIDENCE 2
PHOTO 2: Bare ground + no fire extinguisher / no signage / no spill kit - close-up [ INSERT PHOTO HERE ] DRAG & DROP YOUR SITE PHOTO Fig 09.2 Add: Close-up / Different Angle
BOX 4: RISK LEVEL & IMPACT - CRITICAL
Major fire/explosion risk, catastrophic environmental release, soil/groundwater contamination leading to prosecution. Potential Major Accident Hazard (MAH) - pool fire affecting adjacent works. Immediate danger to life and environment.
BOX 5: REQUIRED CORRECTIVE ACTION
1. STOP all fueling operations - secure area with fire watch and 15m exclusion zone until compliant
2. Provide compliant bunded storage: 110% secondary containment, impervious concrete floor, roofed, ventilated, 15m from drains/buildings
3. Install fire extinguishers (2x 9kg DCP + 1x foam), HAZCHEM signage, spill kit 150L, earthing/bonding system tested
4. Develop and communicate Fuel Storage & Handling SOP + conduct emergency response drill (spill + fire)
5. Location to be approved by SE EHS - minimum 15m from excavations/buildings/drains - risk assessment required
STANDARD REF
• ISO 45001:2018 • ISO 14001:2015 • OSHA 29 CFR 1926 • SE EHS Contractor Req • Project EHS Plan • Local EPA / HSG 176 • SE-GEN-EHS-007
Siemens Energy | Zero Harm | Confidential | Boxed Format - 5 Boxes + 2 Photo Placeholders Per Slide
Slide 09 | SE-EHS-NC-2026

## Slide 11
10
10 - RECURRING VIOLATIONS - PERSISTENT PPE VIOLATIONS DESPITE WARNINGS
RISK: CRITICAL
BOX 1: NON-COMPLIANCE DETAILS - Insert Location/Date/Time
Continued and repeated PPE violations after 3 formal warnings, 5 Safety Observation Cards, 2 NCRs in last 14 days
Same workgroup and supervision involved - indicates intentional non-compliance, not lack of awareness
Trend analysis from Daily EHS Reports: 60% increase in PPE violations in last 2 weeks (5 to 12 per week)
Subcontractor management failing to enforce disciplinary procedure per contract Appendix EHS - no action taken
Demonstrates normalization of deviance - systemic failure, not individual mistake
BOX 2: PHOTO EVIDENCE 1
PHOTO 1: Repeat PPE violation - same crew - evidence of intentional non-compliance [ INSERT PHOTO HERE ] DRAG & DROP YOUR SITE PHOTO Fig 10.1 Add: Date, Time, Location, GPS
BOX 3: PHOTO EVIDENCE 2
PHOTO 2: Trend chart / NCR log showing 60% increase - screenshot from Daily Reports [ INSERT PHOTO HERE ] DRAG & DROP YOUR SITE PHOTO Fig 10.2 Add: Close-up / Different Angle
BOX 4: RISK LEVEL & IMPACT - CRITICAL
Normalization of deviance - precursor to serious injury/fatality (Heinrich/Bird triangle). Total failure of subcontractor safety leadership and culture. If PPE (last line of defense per hierarchy) ignored, higher-level controls will also fail. Project reputation and Siemens Energy Zero Harm commitment at direct risk.
BOX 5: REQUIRED CORRECTIVE ACTION
1. Invoke contractual penalty - stop work for repeat offender crew + mandatory leadership engagement - Subcontractor PM presents corrective plan to SE Management
2. Remove and replace non-compliant supervision - require CVs + EHS competency assessment + interview by SE EHS
3. Implement Behavior-Based Safety (BBS) program with positive/negative reinforcement - daily observations + feedback + recognition
4. Daily management safety walks - Siemens Energy PM + Subcontractor PM - joint walk and documented actions
5. Consider partial termination / back-charge for additional EHS supervision if no improvement in 7 days - prepare contingency replacement crew
STANDARD REF
• ISO 45001:2018 • ISO 14001:2015 • OSHA 29 CFR 1926 • SE EHS Contractor Req • Project EHS Plan • Local EPA / HSG 176 • SE-GEN-EHS-007
Siemens Energy | Zero Harm | Confidential | Boxed Format - 5 Boxes + 2 Photo Placeholders Per Slide
Slide 10 | SE-EHS-NC-2026

## Slide 12
ACTION PLAN & MANAGEMENT DECISION MATRIX - BOXED FORMAT
BOX A: IMMEDIATE (0-24 HOURS)
• STOP WORK all critical violations (PTW, Excavation, Diesel, Leaking Equipment) • Secure hazardous areas - hard barricade + fire watch + 15m exclusion • Remove all non-inducted personnel - 100% gate verification • Ground all leaking equipment - Tag DO NOT USE • Issue formal NCR Level 1 & 2 + contractual warning letter • Convene Emergency EHS Meeting - Subcontractor MD/PM within 24h PHOTO BOX: [Insert photo of stop work order / secured area] DECISION REQUIRED: Approve Stop-Work Authority to EHS
BOX B: SHORT-TERM (1-7 DAYS)
• Full PTW System Audit + Re-Training - all supervisors certified - 80% pass mark • Compliant diesel storage - 110% bund + impervious floor + extinguishers • Reinstate traffic signage - retro-reflective + pedestrian segregation + flagmen • Waste management system - color-coded skips + labeling + focal point • Excavation compliance - hard barricades + ladders every 7.5m + competent person checks • PPE Campaign + BBS Launch - daily checks + scorecard • EHS Directives Log - daily sign-off by PM + EHS PHOTO BOX: [Insert after-correction photos - compliant state] DECISION: Approve $15k cost - back-charge to subcontractor
BOX C: STRATEGIC (7-30 DAYS)
• Contractual Enforcement: Penalty matrix linked to KPIs (TRIR, NCR closure, PTW compliance) • Leadership Accountability: Replace non-performing supervisors - CV + competency interview • System Upgrade: QR/Biometric induction + digital PTW + equipment checklist app • KPI & Scorecard: Weekly dashboard Red/Amber/Green to Top Management • Independent Audit: 3rd party EHS audit ISO 45001/14001 gap analysis • Zero Harm Commitment: Re-sign Life Saving Rules - Townhall with Top Management • Contingency: Prepare demobilization / replacement plan if no improvement PHOTO BOX: [Insert dashboard / training photos] DECISION: Authorize partial termination if critical violations recur
BOX D: MANAGEMENT DECISION MATRIX - REQUIRED TODAY
1. Approve IMMEDIATE Stop-Work Authority to EHS for Critical Violations [ ] Yes [ ] No | 2. Authorize Formal Contractual Warning & Penalty Enforcement [ ] Yes [ ] No | 3. Mandate Subcontractor Top Management Presence On-Site within 48h [ ] Yes [ ] No | 4. Approve Budget for Additional EHS Controls (Bunded Storage, Signage, Barricades) - Back-charge to Subcontractor [ ] Yes [ ] No | 5. Endorse Zero Tolerance Policy: 3 Strikes = Removal - Communicate in Townhall [ ] Yes [ ] No Signature: _________________ Project Director Date: _______ | Signature: _________________ Construction Manager Date: _______ | Signature: _________________ EHS Manager Date: _______