## Slide 1
SIEMENS ENERGY
CONFIDENTIAL
SUBCONTRACTOR EHS NON-COMPLIANCE & SAFETY VIOLATION REPORT
BOXED FORMAT WITH PHOTO PLACEHOLDERS / نسخة مقسمة بخانات وأماكن صور
Project: KAZ Power Plant Upgrade Ref: SE-EHS-NC-2026-001 BOXED V2 Date: September 2026 Prepared by: EHS Manager - Siemens Energy FORMAT: • Each slide = 5 Boxes • Box 1: Non-Compliance Details • Box 2 & 3: Photo Evidence Placeholders (2 photos per violation) • Box 4: Risk Level • Box 5: Corrective Action + Standard Reference
HOW TO USE THIS TEMPLATE / كيفية الاستخدام
1. لكل مخالفة، يوجد 5 خانات واضحة 2. خانة 1: اكتب تفاصيل المخالفة + الموقع + التاريخ 3. خانة 2 و 3: اسحب صورتين من الموقع وألصقهما هنا - صورة 1: نظرة عامة - صورة 2: تفاصيل قريبة / زاوية أخرى 4. خانة 4: مستوى الخطورة تلقائياً ملون 5. خانة 5: الإجراءات التصحيحية + المرجع القانوني DESIGN: • Deep Teal #0E2F3E background • White boxes for actions • Red for CRITICAL, Amber for HIGH • Photo boxes have [INSERT PHOTO HERE] placeholder • Just drag & drop your site photos
Zero Harm is Non-Negotiable | 5 Boxes Per Slide | 2 Photos Per Violation | Ready for Management Decision

## Slide 2
01
01 - UNAUTHORIZED WORK - WITHOUT PERMIT TO WORK (PTW)
أعمال بدون تصريح عمل
RISK: CRITICAL | خطر: CRITICAL
📋 BOX 1: NON-COMPLIANCE DETAILS / خانة تفاصيل المخالفة
• Location: [Add Area] - Date: [Add Date]
• Activity: Excavation / Mechanical / Hot Work without approved PTW
• Violation: No TRA review, no isolation, no SIMOPS check
• PTW logbook not maintained, permit not displayed at work front
• Reference: SE EHS General Requirements Sec 5.3, KAZ EHS Plan Sec 7.2
📷 BOX 2: PHOTO EVIDENCE 1 / صورة 1
PHOTO 1: Work activity without PTW display [ INSERT PHOTO HERE ] Fig 01.1 Add: Date, Time, Location, GPS if possible
📷 BOX 3: PHOTO EVIDENCE 2 / صورة 2
PHOTO 2: PTW Logbook / Missing permit at site [ INSERT PHOTO HERE ] Fig 01.2 Add: Close-up / Different angle
⚠️ BOX 4: RISK LEVEL - CRITICAL / خانة مستوى الخطورة
Fatality, fire/explosion, loss of control. Breach of ISO 45001 Cl 8.1.2. Authority may issue prohibition notice.
✅ BOX 5: REQUIRED CORRECTIVE ACTION / خانة الإجراءات التصحيحية + STANDARD REFERENCE
1. STOP WORK immediately - secure area
2. Re-training PTW for all supervisors in 24h
3. Issue NCR Level 1 + warning letter
4. Daily PTW audit for 14 days
5. 3-strikes removal policy
📚 STANDARD REF
• ISO 45001:2018 • ISO 14001:2015 • OSHA 29 CFR 1926 • SE EHS Contractor Req • Project EHS Plan • Local EPA / HSG
Siemens Energy | Zero Harm | Confidential | Boxed Format with Photo Placeholders
Slide 01 | SE-EHS-NC-2026

## Slide 3
02
02 - SITE ACCESS & INDUCTION - WITHOUT EHS INDUCTION
دخول موقع بدون تدريب السلامة
RISK: CRITICAL | خطر: CRITICAL
📋 BOX 1: NON-COMPLIANCE DETAILS / خانة تفاصيل المخالفة
• No. of persons: [8-12] found working without induction card
• Gate register vs actual headcount mismatch
• No induction sticker / QR verification
• Violation: KAZ EHS Plan Sec 6.1, Local labor law
• System failure: Security-EHS interface weak
📷 BOX 2: PHOTO EVIDENCE 1 / صورة 1
PHOTO 1: Workers without induction cards [ INSERT PHOTO HERE ] Fig 02.1 Add: Date, Time, Location, GPS if possible
📷 BOX 3: PHOTO EVIDENCE 2 / صورة 2
PHOTO 2: Gate register / Induction cards check [ INSERT PHOTO HERE ] Fig 02.2 Add: Close-up / Different angle
⚠️ BOX 4: RISK LEVEL - CRITICAL / خانة مستوى الخطورة
Workers unaware of hazards, emergency assembly, life-saving rules. Risk of unsafe acts + regulatory stoppage. ISO 45001 Cl 7.2/7.3
✅ BOX 5: REQUIRED CORRECTIVE ACTION / خانة الإجراءات التصحيحية + STANDARD REFERENCE
1. Remove all non-inducted personnel now
2. 100% gate check - Security + EHS
3. Submit manpower list vs induction in 12h
4. QR/Biometric tracking system
5. Back-charge re-induction cost
📚 STANDARD REF
• ISO 45001:2018 • ISO 14001:2015 • OSHA 29 CFR 1926 • SE EHS Contractor Req • Project EHS Plan • Local EPA / HSG
Siemens Energy | Zero Harm | Confidential | Boxed Format with Photo Placeholders
Slide 02 | SE-EHS-NC-2026

## Slide 4
03
03 - PPE NON-COMPLIANCE - FAILURE TO WEAR MANDATORY PPE
عدم ارتداء معدات الحماية الشخصية
RISK: HIGH | خطر: HIGH
📋 BOX 1: NON-COMPLIANCE DETAILS / خانة تفاصيل المخالفة
• PPE missing: Helmet chin strap, safety glasses, gloves, hi-vis vest
• Location: [Add location] - Work: [Add task]
• Supervision present but not enforcing
• PPE available in store - behavioral failure
• Violation: SE Life Saving Rule #3, EN 397/166
📷 BOX 2: PHOTO EVIDENCE 1 / صورة 1
PHOTO 1: PPE violation - wide shot [ INSERT PHOTO HERE ] Fig 03.1 Add: Date, Time, Location, GPS if possible
📷 BOX 3: PHOTO EVIDENCE 2 / صورة 2
PHOTO 2: PPE violation - close-up + supervisor present [ INSERT PHOTO HERE ] Fig 03.2 Add: Close-up / Different angle
⚠️ BOX 4: RISK LEVEL - HIGH / خانة مستوى الخطورة
Head injury, eye injury, hand cuts, struck-by. Weak safety culture. Increases LTIFR/TRIR.
✅ BOX 5: REQUIRED CORRECTIVE ACTION / خانة الإجراءات التصحيحية + STANDARD REFERENCE
1. On-spot correction + TBT with photos
2. Issue Observation Card + violation notice
3. Daily PPE checks - start of shift + random
4. Link PPE to KPI & payment milestone
5. Supervisor accountability - 3 strikes
📚 STANDARD REF
• ISO 45001:2018 • ISO 14001:2015 • OSHA 29 CFR 1926 • SE EHS Contractor Req • Project EHS Plan • Local EPA / HSG
Siemens Energy | Zero Harm | Confidential | Boxed Format with Photo Placeholders
Slide 03 | SE-EHS-NC-2026

## Slide 5
04
04 - EXCAVATION SAFETY - INADEQUATE HARD BARRICADES
أعمال حفر بدون حواجز صلبة
RISK: CRITICAL | خطر: CRITICAL
📋 BOX 1: NON-COMPLIANCE DETAILS / خانة تفاصيل المخالفة
• Depth: [1.2m - 2.5m] - No hard barricade, only loose tape (prohibited)
• No edge protection, no ladder for access/egress
• Spoil pile within 1m of edge - surcharge risk
• No reflective markers / lighting at night
• Violation: OSHA 1926 Subpart P, SE-GEN-EHS-007
📷 BOX 2: PHOTO EVIDENCE 1 / صورة 1
PHOTO 1: Excavation without hard barricade - full view [ INSERT PHOTO HERE ] Fig 04.1 Add: Date, Time, Location, GPS if possible
📷 BOX 3: PHOTO EVIDENCE 2 / صورة 2
PHOTO 2: Spoil pile too close + no ladder - close view [ INSERT PHOTO HERE ] Fig 04.2 Add: Close-up / Different angle
⚠️ BOX 4: RISK LEVEL - CRITICAL / خانة مستوى الخطورة
Fatal fall, cave-in engulfment, vehicle fall. High-risk activity - MAH. Authority prohibition risk.
✅ BOX 5: REQUIRED CORRECTIVE ACTION / خانة الإجراءات التصحيحية + STANDARD REFERENCE
1. IMMEDIATE hard barricade - scaffold tubes / concrete
2. Ladders every 7.5m + spoil 1.5m away
3. Excavation permit re-validation + geotech check
4. Reflective delineators + solar lights
5. Competent person checklist daily
📚 STANDARD REF
• ISO 45001:2018 • ISO 14001:2015 • OSHA 29 CFR 1926 • SE EHS Contractor Req • Project EHS Plan • Local EPA / HSG
Siemens Energy | Zero Harm | Confidential | Boxed Format with Photo Placeholders
Slide 04 | SE-EHS-NC-2026

## Slide 6
05
05 - DIRECTIVES NON-COMPLIANCE - FAILURE TO FOLLOW EHS INSTRUCTIONS
عدم الالتزام بتعليمات السلامة
RISK: HIGH | خطر: HIGH
📋 BOX 1: NON-COMPLIANCE DETAILS / خانة تفاصيل المخالفة
• Date of instruction: [Add date] - Instruction: [Add details]
• TBT not conducted / no attendance sheet
• Previous NCRs closed without evidence - falsification
• Verbal + written instructions ignored - documented in daily report
• Violation: ISO 45001 Cl 7.3 & 8.1 - Willful disregard
📷 BOX 2: PHOTO EVIDENCE 1 / صورة 1
PHOTO 1: Evidence of ignored instruction (e.g., open excavation) [ INSERT PHOTO HERE ] Fig 05.1 Add: Date, Time, Location, GPS if possible
📷 BOX 3: PHOTO EVIDENCE 2 / صورة 2
PHOTO 2: TBT register missing / NCR closure without evidence [ INSERT PHOTO HERE ] Fig 05.2 Add: Close-up / Different angle
⚠️ BOX 4: RISK LEVEL - HIGH / خانة مستوى الخطورة
Erosion of EHS authority, culture failure. If directives optional, all critical controls (LOTO, WAH) will fail.
✅ BOX 5: REQUIRED CORRECTIVE ACTION / خانة الإجراءات التصحيحية + STANDARD REFERENCE
1. Formal letter to Subcontractor MD - written commitment
2. Daily EHS Directives Log - sign-off PM + EHS
3. Leadership stand-down with all foremen
4. Link to contractual penalty
5. Weekly scorecard in PM meeting
📚 STANDARD REF
• ISO 45001:2018 • ISO 14001:2015 • OSHA 29 CFR 1926 • SE EHS Contractor Req • Project EHS Plan • Local EPA / HSG
Siemens Energy | Zero Harm | Confidential | Boxed Format with Photo Placeholders
Slide 05 | SE-EHS-NC-2026

## Slide 7
06
06 - TRAFFIC & SIGNAGE - MISSING / DAMAGED SAFETY SIGNS
إشارات مرورية وتحذيرية مفقودة
RISK: HIGH | خطر: HIGH
📋 BOX 1: NON-COMPLIANCE DETAILS / خانة تفاصيل المخالفة
• Missing: Speed limit (15 km/h), parking, pedestrian walkway signs
• No flagmen at intersections / blind spots
• Speeding observed: 30 km/h in 15 km/h zone - radar check
• Pedestrian routes not marked / segregated
• Violation: Project TMP, ISO 39001
📷 BOX 2: PHOTO EVIDENCE 1 / صورة 1
PHOTO 1: Missing / damaged speed limit sign [ INSERT PHOTO HERE ] Fig 06.1 Add: Date, Time, Location, GPS if possible
📷 BOX 3: PHOTO EVIDENCE 2 / صورة 2
PHOTO 2: No pedestrian segregation + speeding area [ INSERT PHOTO HERE ] Fig 06.2 Add: Close-up / Different angle
⚠️ BOX 4: RISK LEVEL - HIGH / خانة مستوى الخطورة
Vehicle-pedestrian collision, equipment damage, fatality - Top 3 fatality cause. Emergency access blocked.
✅ BOX 5: REQUIRED CORRECTIVE ACTION / خانة الإجراءات التصحيحية + STANDARD REFERENCE
1. Reinstate all signs - retro-reflective grade
2. Pedestrian routes with Jersey barriers + green paint
3. Deploy flagmen + radar checks 2x daily
4. Traffic safety campaign + driver re-induction
5. EHS + Logistics joint daily inspection
📚 STANDARD REF
• ISO 45001:2018 • ISO 14001:2015 • OSHA 29 CFR 1926 • SE EHS Contractor Req • Project EHS Plan • Local EPA / HSG
Siemens Energy | Zero Harm | Confidential | Boxed Format with Photo Placeholders
Slide 06 | SE-EHS-NC-2026

## Slide 8
07
07 - WASTE MANAGEMENT - NO SEGREGATION & LABELING
عدم فرز النفايات ووضع ملصقات
RISK: HIGH | خطر: HIGH
📋 BOX 1: NON-COMPLIANCE DETAILS / خانة تفاصيل المخالفة
• Waste mixed: Hazardous + recyclable + general in same skip
• No color-coding, no labeling, no MSDS for haz waste
• Oil rags / filters in general waste - fire + env violation
• Location: [Add waste area location]
• Violation: ISO 14001 Cl 8.1, Project Waste Plan, EPA
📷 BOX 2: PHOTO EVIDENCE 1 / صورة 1
PHOTO 1: Mixed waste in one container - overview [ INSERT PHOTO HERE ] Fig 07.1 Add: Date, Time, Location, GPS if possible
📷 BOX 3: PHOTO EVIDENCE 2 / صورة 2
PHOTO 2: Oil-contaminated rags in general waste - close-up [ INSERT PHOTO HERE ] Fig 07.2 Add: Close-up / Different angle
⚠️ BOX 4: RISK LEVEL - HIGH / خانة مستوى الخطورة
Soil/groundwater pollution, fire from incompatible mixing, regulatory fine, reputational damage, sustainability KPI failure.
✅ BOX 5: REQUIRED CORRECTIVE ACTION / خانة الإجراءات التصحيحية + STANDARD REFERENCE
1. Provide color-coded skips: Black-General, Green-Recyclable, Red-Haz
2. Clean-up & correct segregation under EHS supervision
3. Training on hazardous waste + manifest
4. Appoint Waste Focal Point
5. Weekly waste audit + disposal manifests
📚 STANDARD REF
• ISO 45001:2018 • ISO 14001:2015 • OSHA 29 CFR 1926 • SE EHS Contractor Req • Project EHS Plan • Local EPA / HSG
Siemens Energy | Zero Harm | Confidential | Boxed Format with Photo Placeholders
Slide 07 | SE-EHS-NC-2026

## Slide 9
08
08 - EQUIPMENT INTEGRITY - OIL & FUEL LEAKS FROM MACHINERY
تسريب زيوت ووقود من المعدات الثقيلة
RISK: CRITICAL | خطر: CRITICAL
📋 BOX 1: NON-COMPLIANCE DETAILS / خانة تفاصيل المخالفة
• Equipment: Excavator CAT 320 / Loader [Add ID] - active leak
• Leak type: Hydraulic oil / fuel - dripping observed
• No drip trays, soil contamination ~5 sqm under parking
• No maintenance records, checklist falsified - same signature 7 days
• Violation: PUWER, SE Equipment Standard, ISO 14001
📷 BOX 2: PHOTO EVIDENCE 1 / صورة 1
PHOTO 1: Active oil leak under equipment - with drip [ INSERT PHOTO HERE ] Fig 08.1 Add: Date, Time, Location, GPS if possible
📷 BOX 3: PHOTO EVIDENCE 2 / صورة 2
PHOTO 2: Soil contamination + missing drip tray - parking area [ INSERT PHOTO HERE ] Fig 08.2 Add: Close-up / Different angle
⚠️ BOX 4: RISK LEVEL - CRITICAL / خانة مستوى الخطورة
Fire/explosion (fuel on hot surface), slip, soil pollution, equipment failure loss of control. Maintenance system breakdown.
✅ BOX 5: REQUIRED CORRECTIVE ACTION / خانة الإجراءات التصحيحية + STANDARD REFERENCE
1. Ground equipment - Tag DO NOT USE, remove keys
2. Excavate contaminated soil as haz waste + absorbents
3. Submit maintenance history + 3rd party cert in 48h
4. Daily checklist verified by SE + photo of no leak
5. Drip trays + spill kits at all parking zones
📚 STANDARD REF
• ISO 45001:2018 • ISO 14001:2015 • OSHA 29 CFR 1926 • SE EHS Contractor Req • Project EHS Plan • Local EPA / HSG
Siemens Energy | Zero Harm | Confidential | Boxed Format with Photo Placeholders
Slide 08 | SE-EHS-NC-2026

## Slide 10
09
09 - HAZARDOUS MATERIAL - DIESEL STORAGE WITHOUT BUNDING
خزن الديزل بدون حوض احتواء ثانوي
RISK: CRITICAL | خطر: CRITICAL
📋 BOX 1: NON-COMPLIANCE DETAILS / خانة تفاصيل المخالفة
• Diesel storage: 2000L (2x IBC) - no secondary containment / bunding
• No 110% capacity bund, no impervious base, bare ground
• No fire extinguisher, no HAZCHEM sign, no spill kit
• No earthing/bonding for fuel transfer - static risk
• Ignition source 10m away (welding) - Violation HSG 176, SE-ENV-003
📷 BOX 2: PHOTO EVIDENCE 1 / صورة 1
PHOTO 1: Diesel tanks without bunding - overview [ INSERT PHOTO HERE ] Fig 09.1 Add: Date, Time, Location, GPS if possible
📷 BOX 3: PHOTO EVIDENCE 2 / صورة 2
PHOTO 2: Bare ground + no fire extinguisher / signage - close-up [ INSERT PHOTO HERE ] Fig 09.2 Add: Close-up / Different angle
⚠️ BOX 4: RISK LEVEL - CRITICAL / خانة مستوى الخطورة
Major fire/explosion, catastrophic env release, soil pollution, prosecution, MAH pool fire. Immediate danger to life.
✅ BOX 5: REQUIRED CORRECTIVE ACTION / خانة الإجراءات التصحيحية + STANDARD REFERENCE
1. STOP fueling - 15m exclusion + fire watch
2. Compliant bund: 110%, concrete floor, roofed, ventilated, 15m from drains
3. Install 2x 9kg DCP + foam, HAZCHEM, 150L spill kit, earthing
4. Fuel Handling SOP + emergency drill
5. Location approved by SE EHS + risk assessment
📚 STANDARD REF
• ISO 45001:2018 • ISO 14001:2015 • OSHA 29 CFR 1926 • SE EHS Contractor Req • Project EHS Plan • Local EPA / HSG
Siemens Energy | Zero Harm | Confidential | Boxed Format with Photo Placeholders
Slide 09 | SE-EHS-NC-2026

## Slide 11
10
10 - RECURRING VIOLATIONS - PERSISTENT PPE VIOLATIONS AFTER WARNINGS
مخالفات متكررة رغم التحذيرات
RISK: CRITICAL | خطر: CRITICAL
📋 BOX 1: NON-COMPLIANCE DETAILS / خانة تفاصيل المخالفة
• Same workgroup - 3 warnings + 5 Obs cards + 2 NCRs in 14 days
• Trend: 60% increase (5 to 12 per week) - Daily EHS Reports
• Intentional non-compliance, not lack of awareness
• Subcontractor not enforcing disciplinary procedure per contract
• Indicates normalization of deviance - cultural failure
📷 BOX 2: PHOTO EVIDENCE 1 / صورة 1
PHOTO 1: Repeat PPE violation - same crew [ INSERT PHOTO HERE ] Fig 10.1 Add: Date, Time, Location, GPS if possible
📷 BOX 3: PHOTO EVIDENCE 2 / صورة 2
PHOTO 2: Trend chart / NCR log showing increase [ INSERT PHOTO HERE ] Fig 10.2 Add: Close-up / Different angle
⚠️ BOX 4: RISK LEVEL - CRITICAL / خانة مستوى الخطورة
Precursor to fatality (Heinrich triangle). Total failure of safety leadership. If PPE (last defense) ignored, higher controls will fail. Client confidence at risk.
✅ BOX 5: REQUIRED CORRECTIVE ACTION / خانة الإجراءات التصحيحية + STANDARD REFERENCE
1. Contractual penalty + stop work repeat crew + PM presents plan
2. Remove/replace supervision - CVs + competency interview by SE
3. BBS program - daily observations + feedback + recognition
4. Daily management safety walks - SE PM + Sub PM
5. Prepare partial termination / back-charge if no improvement in 7 days
📚 STANDARD REF
• ISO 45001:2018 • ISO 14001:2015 • OSHA 29 CFR 1926 • SE EHS Contractor Req • Project EHS Plan • Local EPA / HSG
Siemens Energy | Zero Harm | Confidential | Boxed Format with Photo Placeholders
Slide 10 | SE-EHS-NC-2026

## Slide 12
ACTION PLAN & MANAGEMENT DECISION MATRIX - BOXED FORMAT
🔴 BOX A: IMMEDIATE (0-24h) / فوري
• STOP WORK all critical violations • Secure areas - hard barricade + fire watch • Remove non-inducted personnel • Ground leaking equipment - Tag Out • Issue NCR Level 1 & 2 + warning letter • Emergency meeting - Subcontractor MD in 24h PHOTO BOX: [Insert photo of stop work / secured area] DECISION NEEDED: Approve Stop-Work Authority to EHS
🟡 BOX B: SHORT-TERM (1-7 Days) / قصير
• PTW Audit + Re-Training all supervisors • Diesel storage - 110% bund + fire extinguishers • Traffic signs - retro-reflective + flagmen • Waste - color-coded skips + training • Excavation - hard barricades + ladders • PPE Campaign + BBS Launch • EHS Directives Log - daily sign-off PHOTO BOX: [Insert after-correction photos] DECISION: Approve $15k cost - back-charge to sub
🟢 BOX C: STRATEGIC (7-30 Days) / استراتيجي
• Penalty matrix linked to KPIs (TRIR, NCR closure) • Replace non-performing supervisors - competency check • QR/Biometric induction + digital PTW app • Weekly dashboard Red/Amber/Green to Top Mgmt • 3rd party EHS audit ISO 45001/14001 • Re-sign Life Saving Rules - Townhall • Demobilization / replacement contingency plan PHOTO BOX: [Insert dashboard / training photos] DECISION: Authorize partial termination if recur
✅ BOX D: MANAGEMENT DECISION MATRIX - REQUIRED TODAY / مصفوفة قرارات الإدارة المطلوبة اليوم
1. Approve IMMEDIATE Stop-Work Authority to EHS for Critical Violations [ ] Yes [ ] No | 2. Authorize Formal Contractual Warning & Penalty Enforcement [ ] Yes [ ] No | 3. Mandate Subcontractor Top Management On-Site within 48h [ ] Yes [ ] No | 4. Approve Budget for Additional EHS Controls - Back-charge to Subcontractor [ ] Yes [ ] No | 5. Endorse Zero Tolerance Policy: 3 Strikes = Removal - Communicate in Townhall [ ] Yes [ ] No Signature: _________________ Project Director Date: _______ | Signature: _________________ Construction Manager Date: _______